## Slide 2
Workshop:
Cyber-physical Test Benches Remotely Controlled via Internet
Workshop as part of the MYiTOPS project.

## Slide 3
Fist day: Presentation and Group Work
Morning: State of Technology
Definition of Digitalisation
Cyber-physical Systems
Embedded Systems
Fail-safe Communication and Cyber Security
Group Work + Discussion about results
Afternoon: Technical Environment and Cooperation
Current Projects
Test Benches in Karlsruhe
Sensors, Actuators and Interfaces
Network / Internet
Open-Source and GitHub
Groub Work + Discussion about results
Second day (Morning): Practical Introduction
Introduction Github - Hello World
Set up Cyber-physical System with RPI
Set up Network and Server with Labview
Brainstorming and Requirement Analysis
06.11.17
| 3
Workshop is divided into three blocks:

## Slide 4: Definition of Digitalisation
… is the process of converting information into a digital (i.e. computer-readable) format, in which the information is organized into bits… The result is called digital representation or, more specifically, a digital image, for the real object…
“Real World”
Object
“Digital World”
Object
Converting…
Information of the Cat…
Digital transformation
Neugebauer, Reimund. (2018). Digitalisierung: Schlüsseltechnologien für Wirtschaft und Gesellschaft. 10.1007/978-3-662-55890-4 Wikipedia - Digitization
Notes: The Digit-Cat can used to understand Cats, the e-book can used to read the content!

## Slide 5: Examples of established digitisation or digital services today:
Email
E-Commerce
Navigation Systems
Streaming
Language Assistants

## Slide 6: What is particularly important in digitisation?
Form of the data are bits and bytes
Data exchange via a fast and efficient Internet or local Network
Computers and servers are required to process the data
Input and output medium are smartphones, intelligent refrigerators, autonomous cars, smart robots ...

## Slide 7
Digitisation is bringing with it so many major changes that it is seen as the new industrial revolution.
Industry 4.0 is commonly referred to as the fourth industrial revolution.
These revolutions and evolutions include:
  Smart City
  3D-Printer
  AI (Artificial Intelligence)
  Blockchain
  Crypto Currencies
  Fintech (Financial Technology)
  Virtual Reality
  IoT (Internet of Things)
  Cloud Computing
  Big Data
  Smart Home
  Connected Car
  Predictive Maintenance
  Smart Energy

## Slide 8: Conversion of the real information into digital? How?
Industrial revolutions and future view (Industry 4.0 - Wikipedia)

## Slide 9: Definition of Cyber-physical Systems (CPS)
"... linking of real (physical) objects and processes with information processing (virtual) objects and processes via open, partly global and always interconnected information networks"
VDI (Association of German Engineers)

## Slide 10
Neugebauer, Reimund. (2018). Digitalisierung: Schlüsseltechnologien für Wirtschaft und Gesellschaft. 10.1007/978-3-662-55890-4

## Slide 11: What is meant by IoT? Relationship between IoT and CPS?
IoTs are not CPSs, but you can build them with CPSs.
The internet of things is a computing concept that describes the idea of everyday physical objects being connected to the internet and being able to identify themselves to other devices.
Which goal is to be reach by networking and communicating the individual systems depends on the requirements of the overall system.

## Slide 12: What is particularly important in cyber-physical systems (CPS)?
A cyber-physical system represents the desired unity of reality and digital image.
A further development of the mechatronics to a symbiotic system approach on the basis of information technology.
Sensory, actuatorial and cognitive functions can be integrated into technical systems.
Networkability of all components

## Slide 13: The basis for fascinating perspectives of technical systems [3]. Functionalities that have so far only been fulfilled by biological systems:
Autonomous Systems: These systems independently solve complex tasks within of a particular application domain.
Dynamically Networked Systems (System-of-Systems): The degree of system networking will increase. This will result in new, more complex systems, their functionality and performance exceeds the sum of the individual systems.

## Slide 14
Interactive Sociotechnical Systems: Opens up new perspectives on the interaction between human beings and the Machine. The systems will flexibly adapt to the needs of the user.
Product-service Systems : Enables the fusion of material and process services for customer-oriented problem solutions.

## Slide 15: What is the technical basis of the CPSs?
Relationship between embedded systems and CPS[4]
Embedded Systems Design, Peter Marwedel, ISBN 978-3-319-56043-4
Robotics is also a traditional area in which embedded/cyber-physical
systems have been used. Mechanical aspects are very important for robots. Robots, modeled after animals or human beings, have been designed.

## Slide 16: Definition of Embedded Systems (ES)
IEEE has the following definition for embedded systems: An Embedded Computer System: A computer system that is part of a larger system and performs some of the requirements of that system; for example, a computer system used in an aircraft or rapid transit system.
(Institute of Electrical and Electronics Engineers, 1992)
Raspberry Pi 3
Simatic Microbox PC 427B von Siemens

## Slide 17: Examples of Applications of ESs:
Automotive Technology :
ABS (Anti-Lock Braking System)
Adaptive Bend Lighting
ESP (Electronic Stability Program)
Electronic Injection System
Navigation System
Infotainment
Cruise Control
Drive by Wire
Aircraft Technology:
Autopilot
Artificial Horizon
Tail Stabilizer Bars
Wing Dynamics
Infotainment
Engine Control
Mechatronic Monitoring
Automation Technology:
Process control
robotics
Sensor/Actuator Interface
Bluetooth
Buses: Profibus, DeviceNet CANopen, Interbus
e-wire systems
Consumer Goods:
CCD Cameras
Smartphones
MP3 Player
Smarthome Devices
TVs
CD/DVD Systems
Washing Machines
Medicine Technology:
Surveillance Systems
(Monitoring)
Electronic gas dosing
Glucose Testers
Infusion Pumps
Respirators
Incubators
EEG Systems
ECG System
Image: https://www.quora.com/What-is-an-embedded-system

## Slide 18: Main Features of Embedded Computer Systems
Dedicated Function within a larger mechanical or electrical system.
Response Behavior: Realtime, Hard Realtime, i.e. reaction time to requirements/changes.
Fixed Restrictions: size, performance, power, costs.

## Slide 19: Internet and Cyber Security
Cyber security is the basis for successful digitization to protect systems such as
digital production (industry 4.0),
smart energy supply,
logistics and mobility,
health care,
public administration
or cloud-based services.

## Slide 20: The most important protection goals:
Integrity
Confidentiality
Availability
In order to avoid economic and social damage, these points must be guaranteed and must be considered depending on the applications.
Digitisation and networking and the associated link between the digital and physical worlds make it difficult and complex to reach these goals.

## Slide 21: Failsafe und security technical systems. How?
Absolutely closed and self-controlling system?
It is not possible!
Example Connected Car:
Attacks via media interfaces (Bluetooth, USB, WLAN-Hotspots)
Influencing vehicle sensors and Car2X communication
Attacks and changes in physical access to the vehicle
Attacks on backend systems via web (e.g. Smartphone Vehicle Apps)
Faults due to wear and tear (including control mechanisms)
https://www.it-daily.net/it-sicherheit/cyber-defence/18736-die-groessten-gefahren-fuer-die-it-sicherheit-im-connected-car

## Slide 22: The Internet is a public space! Don't forget. What does this mean for a fail-safe and secure connection over the Internet?
"Around the World in 900 Milliseconds"
https://cyber.harvard.edu/digitaldemocracy/internetarchitecture.html
Here's the itinerary for Andrew's intrepid packets -- the path from his laptop to his Harvard mailserver:
1 cobalt03.mn (Magicnet Mongolia) (202.131.0.79) 2 China Satnet (203.222.194.18) 3 China Satnet (203.222.192.97) 4 SATNETEX - China Digital satNet Ltd. (203.222.192.68) 5 DigitalNetworkAlliance.GW.opentransit.net (193.251.252.230) 6 P2-1-0.HKGAR1.Hong-kong.opentransit.net (193.251.241.198) 7 P2-3.HKGBB2.Hong-kong.opentransit.net (193.251.242.189) 8 P13-0.SJOCR2.San-jose.opentransit.net (193.251.242.90) 9 P4-0.SJOCR1.San-jose.opentransit.net (193.251.242.2) 10 P5-0.NYKCR2.New-york.opentransit.net (193.251.251.225) 11 P4-0.NYKCR3.New-york.opentransit.net (193.251.242.253) 12 So2-0-0.ASHBB1.Ashburn.opentransit.net (193.251.248.177) 13 dcp-brdr-01.inet.qwest.net (205.171.209.46) 14 dca-core-01.inet.qwest.net (205.171.9.9) 15 dca-core-03.inet.qwest.net (205.171.8.218) 16 jfk-core-03.inet.qwest.net (205.171.230.6) 17 jfk-core-01.inet.qwest.net (205.171.8.19) 18 bos-core-02.inet.qwest.net (205.171.28.29) 19 bos-edge-02.inet.qwest.net (63.145.1.133) 20 Harvard router (192.5.66.5) 21 border-gw-ge-wan3-1.fas.harvard.edu (140.247.2.5) 22 core-1-gw-vl415.fas.harvard.edu (140.247.2.61) 23 core-nw-gw-vl216.fas.harvard.edu (140.247.216.1) 24 cyber-mail.law.harvard.edu (140.247.216.113)
Too many "computers" involved who can cut off or manipulate the data exchange!

## Slide 23: How can we establish a fail-safe communication and secure connection?
Using cryptographic network protocols: SSH, HTTPS, etc.
Data integrity: Checking the correctness of the data and data structure
Develop autonomous systems related to connection breakdowns
These three points must stay in your head!

## Slide 24
Division into three working groups for each question: processing time 15 min and presentation of the results 10 min for each group.
Group 1:
What is meant by new industrial revolution?
Group 2:
How can technical systems be digitized?
Group 3:
What is the difference between a stable and secure connection?
Notes: Tafel -> saving time, location-independent cooperation, project management, Monitoring development, Coordination of tasks, Scientific added value

## Slide 25: Lunch Break! See you soon…

## Slide 26: Cyber-physical Test Benches Remotely Controlled via Internet
Data acquisition and Controlling via a cyber-physical
system
Converting to digital object…
Remote Control
Transfer digital data …
Server
Peer-to-Peer (P2P)
and encrypted…

## Slide 27
Technical Environment and Cooperation
Current Projects and Test Benches in Karlsruhe
Sensors, Actuators and Interfaces
Network / Internet
Open-Source and GitHub
Groub Work + Discussion about results

## Slide 28: Current Projects (HS)
Remote Control Chain Saw Denis
Environmental Chamber Bruchsal
Remote Control/Monitoring Energy Flows CHP
Load Station Bruchsal
EtaNet CPS-Energy System

## Slide 29: Environmental Chamber Bruchsal
Artur Martel, Arsema Derbie, Dennis Weierter

## Slide 30: Guidelines for „Environmental Chamber“ Project
Ready
LabVIEW controlled Software (Server)
Data backup with SQLite database
Agilent Digital Multimeter
In Process
Raspberry PI (clients) for controlling, data acquisition and networking:
Throttle regulation
Temperature regulation
Etc.

## Slide 31
Dennis Weierter
Remote Control Chain Saw

## Slide 32: Guidelines for „Remote Control Chain Saw“ Project
Ready
Arduino controlled hardware
Servomotors as actuators
Pneumatic cylinder for rope start
With hardware operating unit
In Process
Raspberry PI (clients) for controlling, data acquisition and remote control over the Internet.

## Slide 33
| 13
06.11.17
CHP Efficiency
Mitchell Enrique Kuansin, Ferhat Aslan
https://github.com/IKKUengine/CHPefficiency (Python and LabVIEW)

## Slide 34: Guidelines for „CHP Efficiency“ Project
Ready
Raspberry PI controlled hardware
Gas Flow Meter
Heat Meters
Power Analyzer
Data backup with SQLite database
Data processing via the Labview server
In Process
Remote control over the Internet.

## Slide 35
| 13
06.11.17
CPS Electric Vehicle Charging Station
Pavel Smirnov, Ferhat Aslan
In Process
Management concept for CHP and charging station
Laboratory setup
Remote control over the Internet

## Slide 36: Remote Controlled Accelerator Pedal
In Process
Driving Speed Profile
Laboratory setup
Remote control over the Internet
ECO-WORTHY Linear Actuator
www.pce-instruments.com
Project Group - UMP

## Slide 37: A higher goal is the networking of all cyber physical objects, which allows a collective management.
Scalable Higher-Level System
First foundations were laid with the ηNet project: https://github.com/IKKUengine/SimulatedCPSLabVIEWEnergySystem (LabVIEW, Open Source License MIT)

## Slide 38
Producer
Consumer
Storage
Data Collector
Handler
Monitoring
Management Interface
OOP-oriented Programming Paradigm
Cyber-Physical Objects

## Slide 39: Guidelines for „CPS-Energy System“
Ready
Standardization of communication and control
Interface for a management algorithm
Interface for a data monitoring
Object-oriented observation and programming / parameterization
Data backup with SQLite database
Published as Open-Source
In Process
Access to the entire system via a secure server-side database
First working management algorithm: Combination electric vehicle charging stationwith combined heat an.d power unit

## Slide 40: Sensors, Actuators and Interfaces
How do we get physics into the digital world?

## Slide 41
Overview image board computer car:
http://akautomotiveservices.co.uk/training-courses-vehicle-electrics-module-3/

## Slide 42: How do I get physical or chemical quantities on my computer?
https://www.researchgate.net/figure/Base-physical-quantity-name_tbl1_283195320

## Slide 43: Sensorsystem
Example: Light Sensor
Physical or Chemical Quantity
Conversion to a digital electrical signal: ON/OFF.
Sensors
Light

## Slide 44: Actuatorsystem
Example: Light Actuator
Physical or Chemical Quantity
Conversions to an analogue electrical signal: switch on!
Sending digital electrical signal
Actuators
Switch-on System
Light

## Slide 45: The computer understands only (digital) 0 or 1!
https://www.slideshare.net/AsifIqbal109/digital-to-analog-dac-analog-to-digital-converter-adc

## Slide 46
Sensors and actuators have different interfaces for signal transmission with the computer.
Some of the most common interfaces and protocols are:
RS232
USB
I2C
Ethernet
CAN
Digit I/O
Analog I/O
Etc.

## Slide 47
“Real World”
Object
Cat-data to be sent…
converting over the interfaces
Information of the Cat…
Back to our cat:

## Slide 48: Send the Cat-data to Germany now!
It's very complex!?

## Slide 49: Internet? Any computer can connect to any other computer.
https://en.wikipedia.org/wiki/Peer-to-peer
Peer-to-peer (P2P) network
Network based on the client-server model
Peers are equally privileged, equipotent participants in the application.
Individual clients request services and resources from centralized servers.
There are two connection types:

## Slide 50
A set of commands exists to control communication between two devices, e.g. between two computers.
How do computers interact?

## Slide 51: Internet Protocol
https://en.wikipedia.org/wiki/Internet_Protocol
It's very complex!? Yes and no…
The rules or set of commands are grouped together in the Internet Protocol family.

## Slide 52: “Imagine, TCP is the data. IP is the Internet location GPS.”
https://www.hostingadvice.com/blog/tcpip-make-internet-work/
The Link Layer is the physical network equipment used to interconnect nodes and servers.
The Internet Layer connects hosts to one another across networks.
The Transport Layer resolves all host-to-host communication.
The Application Layer is utilized to ensure communication between applications on a network.
It's easier to think in layer:

## Slide 53
For us is only important to use the tools that can these rules.
LabVIEW make it easy, just lern it.
A simple higher layer (like building blocks) makes the development uncomplicated.
https://stackoverflow.com/questions/30994389/labview-programming
„Malaysia“
„Germany“
Internet

## Slide 54
Python make it easy, just lern it.
https://www.bogotobogo.com/python/python_network_programming_server_client.php
Server-Code
Client-Code
Internet
The same as LabVIEW only with text code…
„Germany“
„Malaysia“

## Slide 55: More in the third block: Practical Introduction

## Slide 56
How can we work together between Germany and Malaysia?
How do we stay in touch?
How do we divide the work between us? Workflow?
How can everyone always be very well informed about the status of projects and members?

## Slide 57: Solution…

## Slide 58
https://kinsta.com/knowledgebase/what-is-github/
What is GitHub?
It lets you and others work together on projects from anywhere.
GitHub is a website and cloud-based service:
Store,
manage,
track and
control changes of your project documents.
To understand exactly what GitHub is, you need to know two connected principles:
Version control
Git

## Slide 59
https://en.wikipedia.org/wiki/Version_control
What Is Version Control?
Collaboration with repositories and handful of commands!
Also known as revision control or source control, is the management of changes to documents, computer programs, large web sites, and other collections of information (Wikipedia.org).
pull
init
push
commit
branche
merge

## Slide 60: Repositories
https://prewajdena.cf/wireless/351contrile-de-version-avec-tilichargement-github.html
Colloquially known as a "repo" for short.
Repo is a "directory or memory" with additional properties.
Alice, David, Bob and Clair can create a clone repo from the original to the local computer
They can continue the development locally. Time parallel!
In the meantime, if something changes in the origin (also among subteams). Then it can be fetched via "pull".

## Slide 61
Repo is a "directory or memory" with additional properties? You can do many things…
Let's cook with Git.
Init „RepoTable “
Commit „Create empty table“
Add to „RepoTable“ milk, eggs and soup
Your partner wants to help you
you order rice for the meal, but you don't want to be disturbed
Branch “RiceBranch” revision r4 to r5
Clone “RiceBranch”: Now the branch can be copied or cloned on local development machines
Add to “RiceBranch” rice (r6)
Commit „I cooked rice“
Merge it to (r7) „RepoTable“ (->r8)
Enjoy your meal…

## Slide 62
With which tool can ofline work on the local computer to simply then update the Origin on the server?
https://git-scm.com/downloads
https://git-scm.com/docs/gittutorial
But we only learn the handling in the workshop via the platform. More in the third block: Practical Introduction…

## Slide 63
An example: The creation of this presentation.

## Slide 64
Group 1:
What is meant by analog and digital signals?
Group 2:
What is meant here by server and client and how can communication via the Internet be made easy?
Group 3:
What can we do together to establish an active
cooperation?
Division into three working groups for each question: processing time 15 min and presentation of the results 10 min for each group.

## Slide 65: Brainstorming and Requirement Analysis for Remote Controlled Test Benches between HS and UMP (15 min)
1. Step
Brainstroming: With regard to the technical possibilities in HS and UMP - > Ideas for test benches / systems and their implementation
2. Step
Concrete requirement analysis for the system ideas: measured variables, measurement technology, controlling, time management
Moderator summarizes all ideas on the board.

## Slide 66: Software Publications
GitHub.com/ikkuengine
https://github.com/IKKUengine/SimulatedCPSLabVIEWEnergySystem (LabVIEW)
https://github.com/IKKUengine/CHPefficiency (Python)
Will follow soon:
https://github.com/IKKUengine/SingleServerCHPefficiency (LabVIEW)
https://github.com/IKKUengine/ThreadedEtaNetServer (C++/Qt5.8)
https://github.com/IKKUengine/CPOEtaNetClient (C++/Qt5.8)

## Slide 67
Dankeschön…
Contact
Ferhat Aslan
Institut für Kälte-, Klima- und Umwelttechnik
Tel.: 0721 925-1815
Raum M-U07
E-Mail: ferhat.aslan@hs-karlsruhe.de
Prof. Dr.-Ing. Maurice Kettner
Fakultät für Maschinenbau und Mechatronik
Tel.: 0721 925-1845
Raum F-111
E-Mail: maurice.kettner@hs-karlsruhe.de